## Slide 1: Barriers to brain volume measurement in the real world
M. Battaglini
QNL- Quantitative Neuroimaging Lab, Department of Medicine, Surgery and Neurosciences, University of Siena

## Slide 2: Disclosure
Nothing to declare

## Slide 3
Review of the most important barriers to the use of atrophy measurement in the real world:
list and possible solutions
Definition of measurement for a MR image.
Normative rates of atrophy: a lack for the clinical use of brain volume measurement in the
real world

## Slide 4
Definition of measurement for a MR image.
Review of the most important barriers to the use of atrophy measurement in the real world:
list and possible solutions
Normative rates of atrophy: a lack for the clinical use of brain volume measurement in the
real world

## Slide 5: Quantification of a measure
Thing to be measured: TABLE
Thing that measures: RULER

## Slide 6: Quantification of a measure
Thing to be measured: TABLE
Thing that measures: RULER
✖️
=
Length of the table

## Slide 7: Quantification of a measure
Thing to be measured: TABLE
Thing that measures: RULER
✖️
=
Changes in length if measured in summer (bigger)
or in winter (smaller)
The length will have the error of the scale.
Example: If the scale is 10 cm long, you cannot say if the table is 204
or 196 cm but only 200 cm ± 5 cm
Length of the table

## Slide 8: Quantification of a measure
Thing to be measured: TABLE
Thing that measures: RULER
✖️
=
Measure of the length of table= True length + “Physiological” variation + error of the Ruler
Length of the table
Changes in length if measured in summer (bigger)
or in winter (smaller)
The length will have the error of the scale.
Example: If the scale is 10 cm long, you cannot say if the table is 204
or 196 cm but only 200 cm ± 5 cm

## Slide 9: Quantification of a measure for MR images
✖️
is it correct?

## Slide 10: Quantification of a measure for MR images
✖️
is it correct? NO

## Slide 11: Quantification of a measure for MR images

## Slide 12: Quantification of a measure for MR images
〰️

## Slide 13: Quantification of a measure for MR images
〰️

## Slide 14: Quantification of a measure for MR images
〰️

## Slide 15: Quantification of a measure for MR images
〰️
Different field strength of the magnet

## Slide 16: Quantification of a measure for MR images
〰️
Different hardware architecture of the magnet
Different field strength of the magnet

## Slide 17: Quantification of a measure for MR images
〰️
Different sequences
Different hardware architecture of the magnet
Different field strength of the magnet

## Slide 18: Quantification of a measure for MR images
〰️
Different sequences
Within the same sequence, different acquisition parameters
Different hardware architecture of the magnet
Different field strength of the magnet

## Slide 19: Quantification of a measure for MR images
〰️

## Slide 20: Quantification of a measure for MR images
〰️

## Slide 21: Quantification of a measure for MR images
〰️

## Slide 22: Quantification of a measure for MR images
〰️
There is not a gold standard algorithm to analyse 3D images

## Slide 23: Quantification of a measure for MR images
〰️
There is not a gold standard algorithm to analyse 3D images
Different methods provide different measures for the same analysed image.

## Slide 24
Definition of measurement for a MR image.
Key point: the measurement is not “objective” but depends on:
the MR setting
the software used to analyse the images

## Slide 25
Definition of measurement for a MR image.
Review of the most important barriers to the use of atrophy measurement in the real world:
list and possible solutions
Normative rates of atrophy: a lack for the clinical use of brain volume measurement in the
real world

## Slide 26: Barriers to the use of brain volume in real world

## Slide 27: Barriers to the use of brain volume in real world

## Slide 28: Barriers to the use of brain volume in real world
Change of Volume= True atrophy + Physiological variation + Software error

## Slide 29
+
Barriers to the use of brain volume in real world
Variations due to the Image Acquisition
Change of Volume= True atrophy + Physiological variation + Software error

## Slide 30: Barriers to the use of brain volume in real world
+
+
Variations due to the Image Acquisition
Change of Volume= True atrophy + Physiological variation + Software error
Errors due to the Image Acquisition

## Slide 31
Change of Volume= True atrophy +
Barriers to the use of brain volume in real world
+
+
Variations due to the Image Acquisition
Change of Volume= True atrophy + Physiological variation + Software error
Errors due to the Image Acquisition

## Slide 32: Barriers to the use of brain volume in real world
Change of Volume= True atrophy +
+
+
Variations due to the Image Acquisition
Change of Volume= True atrophy + Physiological variation + Software error
Errors due to the Image Acquisition

## Slide 33: Barriers to the use of brain volume in real world
Change of Volume= True atrophy +
+
+
Change of Volume= True atrophy + Physiological variation + Software error
Variations due to the Image Acquisition
Errors due to the Image Acquisition

## Slide 34: Physiological variation.
De Stefano et al CNS Drugs 2017

## Slide 35: Physiological variation. Example 1 dehydration
Nakamura et al. Neuroimage Clin. 2014
Dehydrated -> Rehydrated
PBVC +0.36%

## Slide 36: Physiological variation. Example 2 circadian rhythms
On 834 AD, the brain parenchyma
fraction (BPF) decreased of -0.221%
per 12 hours.
Nakamura et al. Neuroimage 2015

## Slide 37
Physiological variation
Review of the most important barriers to the use of atrophy measurement
in the real world: list and possible solutions
SOLUTION: to be included in the experimental design

## Slide 38
Change of Volume= True atrophy + Physiological variation + Software error
+
+
Variations due to the Acquisition
Change of Volume= True atrophy +
Barriers to the use of brain volume in real world
Errors due to the Image Acquisition

## Slide 39
 | Features
Manual methods | 
Bicaudate ratio | The minimum intercaudate distance divided by brain width along same line
Brain width | Distance between two points on the cortical surface, measured at the same level as lateral ventricle width on axial slides
Corpus callosum area | Measured on midsagital T1-weighted image
Training of the hippocampus, amygdata, entothinal cortex, paraippocampus, cholinergic nuclei of the basal forebrain | Several anatomical protocols available for delineation of these structures
M/P | Ratio of midbrain-to-pons areas measured on midsagital T1-weighted image
MCP width | Distance between the superior and inferior borders of the MCP, as delimited by the peripeduncular CSF spaces of the pontocerebellar cisterns
MRPI | Value obtained by multiplying the pons to midbrain areas by the MCP-to-SCP widths
Third and lateral ventricle width | Determined along a plane corresponding to the anteroposterior midpoint of the ventricle on axial slices
Semi automated methods | 
Anatomatic | Segmentation algorithm for ventricles
Cavalieri method | Stereological method where brain volumes are obtained by the sum of the points counted on all the sections of the structure of interest multiplied by the sectioning intervals
Fuzzy connectedness | An operator identifies points of GM, WM and CSF, each of which is then automatically detected as a fuzzy connected object
ILAB4 | Segmentation of thin-slice T1-weighted images based on a modifies watershed transform and an automatic histogram analysis
Losseff method | A large central volume of the brain is defined based on anatomical criteria
MIDAS | Thresholding technique for measurement of ventricle volumes
SABRE | Use of individualized Talairach brain maps for brain regions in each hemisphere
Seed growing technique | Intensity threshold-based algorithm propagating from a seed positioned in any part of the brain parenchyma
Automated methods | 
Alfano method | Multispectral methods based on the relaxometric features of brain tissues
BBSI | Measurement of total volume difference between serial scans
BICCR | Digital morphometry for intracerial cavity classification and Bayesian tissue classification into GM, WM, lesions and CSF
BPF | Ratio of the volume of parenchymal brain tissue to the total volume within the outer surface of the brain
BICVR | Ratio of brain volume to intracranial volume
Central cerebral volume | Volume of four to seven (depending on the thickness) axial slices from the central portion of the brain
Chupin methos | Use of simultaneous region deformation driver by probabilistic and anatomical priors for hippocampus and amygdala segmentation
CIVET algorithm | Series of algorithms for corticomeatric analysis of MRI images including tissue classification and segmentation
Cortical pattern matching | Surface-based cortical modelling and 3D GM mapping
DBM | Variant of VBM in which brain volumes are compared on the basis of the deformation fields required to register them onto a common template
FIRST | Subcortical brain segmentation using Bayesian shape and appearance models
Freesurfer | Calculation of the cortical thickness after inflation of the folded cortical surface
HAMMER | High-dimensional warping of brain images producing gyral and subcortical brain structures and tissue density maps
Histogram segmentation | Brain extraction and segmentation technique optimised for 2D T1-weighted images
IBA | Percent ratio of the supratentorial brain parenchyma to supratentorial parenchyma and CSF
Localinfo | Entropy-based segmentation algorithm for subcortical brain structures
Segmentation propagation | Deformation field applied to the segmentation of the baseline brain and then automatically propagated through serial images to provide an estimate of volume change
SIENAx | Global and tissue-type volumes normalised for subject head size
SIENA, SIENAr | Percent brain volume change (PBVC) assessed by estimating the local shift in brain edges across the brain and its voxelwise extension for regional assessment
SPM-based segmentation | Prior spatial information are used to classify voxels according to their location and signal intensity features as GM, Wm and CSF
STAND score | Score based in the voxelwise degree and pattern of atrophy of a scan in comparison to the scans of a large database of well characterised AD and cognitively normal subjects
Support vector machines | Multidimensional classification of cerebral region (e.g. hippocampus) shape features
TDS | Brain tissues are identified by projecting anatomically labelled images of a template brain onto images of the patients brain
3DVIEWNIX | A data-, machine- and application-independent software system for the visualization and analysis of multidimensional images
VBM | Characterising regional volume and tissue ‘concentration’ differences throughout global brain
WBR | Ratio of the difference between intradural and CSF volumes to intradural volumes
MRI-based methods for measuring brain volumes
Error of Software
Which software?

## Slide 40: Error of Software
1) CROSS-SECTIONAL ANALYSIS
2) LONGITUDINAL ANALYSIS
SEGMENTATION METHOD
SEGMENTATION METHOD
REGISTRATION METHOD

## Slide 41: Error of Software
1) CROSS-SECTIONAL ANALYSIS
2) LONGITUDINAL ANALYSIS
SEGMENTATION METHOD
SEGMENTATION METHOD
REGISTRATION METHOD
Error ~ 0.5-1%

## Slide 42: Error of Software
1) CROSS-SECTIONAL ANALYSIS
2) LONGITUDINAL ANALYSIS
SEGMENTATION METHOD
SEGMENTATION METHOD
REGISTRATION METHOD
Error ~ 0.1-0.5%

## Slide 43: Error of Software
Each software can be optimised depending on the studied population

## Slide 44: Error of Software
Each software can be optimised depending on the the studied population

## Slide 45: Error of Software
Each software can be optimised depending on the studied population

## Slide 46: Error of Software
Each software can be improved in order to address the peculiar
MRI features of patients
Each software can be optimised depending on the studied population

## Slide 47: Error of Software: MRI of MS patients
GM
WM
Lesion
Nakamura et al. Neuroimage 2009

## Slide 48: Error of Software: MRI of MS patients
Nakamura et al. Neuroimage 2009, Battaglini et al. HBM 2012
GM
WM
Lesion

## Slide 49: Error of Software: MRI of MS patients
Methods | Global WM intensity distribution | Local WM intensity distribution
Gaussian Kernel Based | Chard et al (J Mag Res Imaging, 2010) | Sdika et al (Human Brain Mapping 2009)
Non parametric |  | Battaglini et al (Human Brain Mapping 2012)

## Slide 50
optimise the software parameters for the specific analysis
Do not change version of the software during the experiment
Physiological variation
Review of the most important barriers to the use of atrophy measurement
in the real world: list and possible solutions
SOLUTION: to be included in the experimental design
Error of the software
SOLUTION:

## Slide 51: Quantification of a measure for MR images
Change of Volume= True atrophy +
+
+
Change of Volume= True atrophy + Physiological variation + Software error
Variations due to the Image Acquisition
Errors due to the Image Acquisition

## Slide 52: Variations due to the acquisition
Can the atrophy measurement be affected by:
1) Different vendor
2) Different Magnetic Strength
3) Different acquisition parameters

## Slide 53: Variations due to the acquisition
Can the atrophy measurement be affected by:
1) Different vendor?
2) Different Magnetic Strength
3) Different acquisition parameters
Potvin et al, NeuroImage 2016
Thalamus L: Not significant
Thalamus R: -250 mm3
(Philips Vs Siemens)

## Slide 54: Variations due to the acquisition
Can the atrophy measurement be affected by:
1) Different vendor? YES (due to different coil, changing SNR)
2) Different Magnetic Strength
3) Different acquisition parameters

## Slide 55: Variations due to the acquisition
Can the atrophy measurement be affected by:
1) Different vendor
2) Different Magnetic Strength?
3) Different acquisition parameters

## Slide 56: Variations due to the acquisition
Can the atrophy measurement be affected by:
1) Different vendor
2) Different Magnetic Strength?
3) Different acquisition parameters
Potvin et al, NeuroImage 2016
Hippocampus L: -234 mm3
Hippocampus R: -298 mm3

## Slide 57: Variations due to the acquisition
Can the atrophy measurement be affected by:
1) Different vendor
2) Different Magnetic Strength? YES (due to improved tissue contrast in 3T)
3) Different acquisition parameters

## Slide 58: Variations due to the acquisition
Can the atrophy measurement be affected by:
1) Different vendor
2) Different Magnetic Strength
3) Different acquisition parameters?

## Slide 59: Variations due to the acquisition
Can the atrophy measurement be affected by:
1) Different vendor
2) Different Magnetic Strength
3) Different acquisition parameters?

## Slide 60: Variations due to the acquisition
Can the atrophy measurement be affected by:
1) Different vendor
2) Different Magnetic Strength
3) Different acquisition parameters?

## Slide 61: Variations due to the acquisition
Can the atrophy measurement be affected by:
1) Different vendor
2) Different Magnetic Strength
3) Different acquisition parameters?
PBVC= -10%

## Slide 62: Variations due to the acquisition
Can the atrophy measurement be affected by:
1) Different vendor
2) Different Magnetic Strength
3) Different acquisition parameters? YES (Different TR and TE, with
the same vendor and magnetic strength, give different tissue contrast!)

## Slide 63
optimise the software parameters for the specific analysis
Do not change version of the software during the experiment
Physiological variation
Review of the most important barriers to the use of atrophy measurement
in the real world: list and possible solutions
SOLUTION: to be included in the experimental design
Error of the software
Variation due to the image acquisition:
SOLUTION:
do not change hardware and software MRI equipment over time;
set the best parameters to obtain high SNR and CNR.
SOLUTION:

## Slide 64: Quantification of a measure for MR images
Change of Volume= True atrophy +
+
+
Change of Volume= True atrophy + Physiological variation + Software error
Variations due to the Image Acquisition
Errors due to the Image Acquisition

## Slide 65: Errors due to the image acquisition
artifacts
Partial head
Solutions: post-processing software
(e.g. N3, FAST, SPM)
depends on coil architecture
the acquired image has strong
intensity inhomogeneities
due to magnetic
susceptibility differences
Solution: gradient correction
during the acquisition, post-processing
software (FAST)
poor shimming, gradient coil heating,
patient motion, reconstruction error, eddy corrent
Solution: to acquire again the image
MR field strength, type of coil,
parameter acquisitions (TR and TE)
Solution: to use MR scanner with higher field, to set carefully parameters of your acquisition (TR, TE)

## Slide 66
Acquisition problem
Time 0
Time 1
Errors due to the acquisition
Bad repositioning can bias atrophy
measurement

## Slide 67
optimise the software parameters for the specific analysis
Do not change version of the software during the experiment
Physiological variation
Review of the most important barriers to the use of atrophy measurement
in the real world: list and possible solutions
SOLUTION: to be included in the experimental design
Error of the software
Variation due to the image acquisition:
do not change hardware and software MRI equipment over time;
set the best parameters to obtain high SNR and CNR.
Errors due to the acquisition
SOLUTION:
Use the gradient correction option during the MR acquisitions
Perform quality control (check for movement artifact, bad repositioning)
Perform appropriate post-processing for improving MRI quality
SOLUTION:
SOLUTION:

## Slide 68
Definition of measurement for a MR image.
Review of the most important barriers to the use of atrophy measurement in the real world:
list and possible solutions
Normative rates of atrophy: a lack for the clinical use of brain volume measurement in the
real world

## Slide 69
BV loss < 35y = ~0
BV loss > 35y = ~0.2
Normative rates of atrophy

## Slide 70
Specificity= probability of being below the cutoff for an HC
Sensitivity= probability of being above the cutoff for a MS patient
De Stefano et al JNNP 2016
Normative rates of atrophy
MS patients: 206
Healthy Control: 35
Long follow-up > 6 years
Same scanner: Philips 1.5T

## Slide 71
Battaglini et al, P529
Normative rates of atrophy
Healthy Controls: n=386
Variable follow-up:
median 1.1 y; (0.5y – 12y)
Different MR setting

## Slide 72
  Multicentre data from HC at different age and magnetic field strength show significant variability, explaining the difficulties in using atrophy rate for single patient assessment.
  Statistical models can provide normative data that take into account all these variables.
  For atrophy rates, the variability decreases with increases of follow-up length. Data at 3T seem to be less variable than data at 1.5T
  .
Normative rates of atrophy: a lack for the clinical use of brain volume measurement in the
real world

## Slide 73: Take home message:
Group analysis
Single subject analysis
Work in progress
The impact of the barriers to brain volume measurement in the real world can be drastically reduced by:
carefully designing the experiment
carefully setting the MR scan and sequences
using dedicated, optimised software
Normative data are essential for better characterizing the individual course
of the atrophy

## Slide 74: MCQ-1 Quantification of atrophy in longitudinal setting.
Which is the most precise and robust method for evaluating whole brain volume changes over time on MRI?
Segmentation method
Registration method
None of them, all the methods have the same magnitude of error.

## Slide 75: MCQ-1 Quantification of atrophy in longitudinal setting.
Which is the most precise and robust method for evaluating whole brain volume changes over time on MRI?
Segmentation method
Registration method
None of them, all the methods have the same magnitude of error.

## Slide 76: MCQ-2 Error of segmentation on MRI of MS patients
Does the lesion filling permit a better evaluation of
CSF?
Whole brain?
GM and WM separately?
optic nerve?

## Slide 77: MCQ-2 Error of segmentation on MRI of MS patients
Does the lesion filling permit a better evaluation of
CSF?
Whole brain?
GM and WM separately?
optic nerve?

## Slide 78: MCQ-3 Reduction of source of variability
A more robust quantification of atrophy can be obtained by:
an accurate repositioning of the subject in the scan
an accurate post-processing to remove Magnetic field inhomogeneity
strictly keeping the same sequences during different MRI sessions
All of them

## Slide 79: MCQ-3 Reduction of source of variability
A more robust quantification of atrophy can be obtained by:
an accurate repositioning of the subject in the scan
an accurate post-processing to remove Magnetic field inhomogeneity
strictly keeping the same sequences during different MRI sessions
All of them